## Slide 1: TSKS14 Multiple Antenna Communications
Lecture 12, 2020
Emil Björnson

## Slide 2: Outline of this lecture
Evolution of cellular networks
  Three ways to make improvements
  The role of multiple antennas
Summary of main benefits of multiple antenna communications
Outlook towards the future

## Slide 3: Martin Cooper’s law
The number of data connections has doubled every 2.5 years
  Since beginning of wireless
  Annual growth: +32%

## Slide 4: Cellular networks
Proposed in 1950s
First deployed in late 1970s

## Slide 5: Current trends
26% annual growth (slower than in the past)
  5 GB/month/person
  20 GB/month/person

## Slide 6: Evolving cellular networks for higher traffic
Increase network throughput [bit/s/km2]
  Consider a given area
Simple formula for network throughput:
How to achieve a 100x improvement?

## Slide 7: Higher cell density
Traditional way to improve throughput
Cut cell radius by  times more cells
Issues: High rent and deployment costs Interference is getting worse WiFi + Cellular is already dense: Coverage is the issue!

## Slide 8: More spectrum
Range suitable for coverage: GHz
Far above 5 GHz: High propagation losses  Mainly short-range hotspots
2G/3G/4G/WiFi
FM radio
…
400-800 THz
Visible light
mmWave spectrum
Range considered in 5G
MIMO plays different roles in different bands

## Slide 9: Higher spectral efficiency
Point-to-point spectral efficiency:
  Governed by capacity limit:
  Increasing signal power:
bit/s/Hz  bit/s/Hz requires more power!
Use multiple antennas instead!

## Slide 10: Fixed beamforming
Fixed beam
with 16 dBi gain
Lucky users
16 dB = 40 times stronger signal
Unlucky users
No benefit from antenna gain
We need adaptive beamforming!

## Slide 11: Evolution of “active” antenna technology
Sector antenna
8 elements (7 dBi each)
1 transceiver chain
Fixed beam 16 dBi
Classical antenna array
64 elements (32 per polarization)
8 transceiver chains (2 per column)
Up to 8 horizontal beams
Massive antenna array
64 elements
64 transceiver chains
Up to 64 3D beams
1 antenna
8 antennas
64 antennas

## Slide 12: Massive MIMO in 5G
64 antennas
Photo: Erik G. Larsson, May 2018

## Slide 13: Different aspects: Multiple antenna communications
Point-to-point scenario
  SIMO, MISO, MIMO
Multi-user scenario
  -antenna base station, single-antenna terminals
Channel modeling
  Deterministic and random channels
  Capacity, outage capacity, ergodic capacity

## Slide 14: Point-to-point: Better user performance
Beamforming and multiplexing gain

## Slide 15: Summary: Point-to-point MIMO
Advantages
  Multiplexing gain and beamforming gain
  Increases capacity for a single user
  Only receiver needs channel state information
Disadvantages
  Hard to fit many antennas into a user terminal
  might only have a few large eigenvalues

## Slide 16: Multi-user MIMO: Spatial multiplexing of users
Few antennas (elements): Broad beams
Massive number of antennas: Narrow beams
Serve many users at same time/frequency resource
Narrow beams limit interference

## Slide 17: Summary: Multi-user MIMO
Advantages
  Multiplexing gain and beamforming gain: Increases sum capacity
  Very scalable technology, any number of antennas, tens of users
  Only base station needs channel state information
Disadvantages
  Capacity per user does not grow as fast
  Require many active users to achieve gains
  Must be implemented in the right way (TDD, etc.)

## Slide 18: Summary: Fading channels
Slow fading
  Outage probability
  Outage capacity
Fast fading
  Ergodic capacity
  Coherence intervals
Diversity gains:

## Slide 19: What have we not covered in the course?
Point-to-point MIMO
  Cases with imperfect channel knowledge
Massive MIMO
  More advanced processing (zero-forcing, MMSE)
  More realistic channels (correlated Rayleigh fading)
Fading channels
  Gradual variations, channel tracking and prediction

## Slide 20: What will happen in the future?
New deployment concepts
1) Distributed Massive MIMO
(Cell-free)
3) Extremely large aperture arrays
2) Intelligent reflecting surface
64-antenna
Massive MIMO

## Slide 21
End of Lecture 12
TSKS14 Multiple Antenna Communications